## Slide 1: CPU Caches
Jamie Allen
@jamie_allen
http://github.com/jamie-allen
JavaZone 2012

## Slide 2: Agenda
Goal
Definitions
Architectures
Development Tips
The Future

## Slide 3: Goal
Provide you with the information you need about CPU caches so that you can improve the performance of your applications

## Slide 4: Why?
Increased virtualization
  Runtime (JVM, RVM)
  Platforms/Environments (cloud)
Disruptor, 2011
Notes: To improve performance, we need to understand the impact of our decisions in the physical world
My goal is help everyone understand how each physical level of caching within a CPU works
Capped the talk below virtual memory (memory management for multitasking kernels), as that is specific to the operating system running on the machine
Not enough time to cover all of the levels of caching that exist on CPUs

## Slide 5
Definitions

## Slide 6: SMP
Symmetric Multiprocessor (SMP) Architecture
Shared main memory controlled by single OS
No more Northbridge
Notes: 2011 Sandy Bridge and AMD Fusion integrated Northbridge functions into CPUs, along with processor cores, memory controller and graphics processing unit
Gil Tene of Azul claims the Vega architecture is a true SMP compared to those of AMD/Intel – circular architecture with linkages between every core

## Slide 7: NUMA
Non-Uniform Memory Access
The organization of processors reflect the time to access data in RAM, called the “NUMA factor”
Shared memory space (as opposed to multiple commodity machines)
Notes: NUMA architectures have more trouble migrating processes across sockets because L3 isn’t warmed
Initially, it has to look for a core with the same speed accessing memory resources and enough resources for the process; if none are found, it then allows for degradation

## Slide 8: Data Locality
The most critical factor in performance
Not guaranteed by a JVM
Spatial - reused over and over in a loop, data accessed in small regions
Temporal - high probability it will be reused before long
Notes: All algorithms are dominated by that - you have to send data somewhere to have an operation performed on it, and then you have to send it back to where it can be used

## Slide 9: Memory Controller
Manages communication of reads/writes between the CPU and RAM
Integrated Memory Controller on die
Notes: Memory controllers were moved onto the processor die on AMD64 and Nehalem

## Slide 10: Cache Lines
32-256 contiguous bytes, most commonly 64
Beware “false sharing”
Use padding to ensure unshared lines
Transferred in 64-bit blocks (8x for 64 byte lines), arriving every ~4 cycles
Position in the line of the “critical word” matters, but not if pre-fetched
@Contended annotation coming to JVM?
Notes: Be careful about what's on them, because if a line holds multiple variables and the state of one changes, coherency must be maintained, killing performance for parallel threads on an SMP machine
If the critical word in the line is in the last block, takes 30 cycles or more to arrive after the first word. However, the memory controller is free to request the blocks in a different order. The processor can specify the "critical word", and the block that word resides in can be retrieved first for the cache line by the memory controller. The program has the data it needs and can continue while the rest of the line is retrieved and the cache is not yet in a consistent state, called "Critical Word First & Early Restart”
Note that with pre-fetching, the critical word is not known - if the core requests the cache line while the pre-fetching is in transit, it will not be able to influence the block ordering and will have to wait until the critical word arrives in order; position in the cache line matters, faster to be at the front than the rear

## Slide 11: Cache Associativity
Fully Associative: Put it anywhere
Somewhere in the middle: n-way set-associative, 2-way skewed-associative
Direct Mapped: Each entry can only go in one specific place
Notes: Replacement policy determines where in the cache an entry of main memory will go
Tradeoff - if data can be mapped to multiple places, all of those places have to be checked to see if the data is there, costing power and possibly time; but more associativity means less cache misses
Set associative has a fixed number of places and can be 2-16-way; skewed does as well, but uses a hash to place the second cache line in the group, only up to 2-way that I know of

## Slide 12: Cache Eviction Strategies
Least Recently Used (LRU)
Pseudo-LRU (PLRU): for large associativity caches
2-Way Set Associative
Direct Mapped
Others
Notes: LRU can be expensive, tracks each cache line with “age bits” - each time a cache line is used, all others have to be updated
PLRU is used where LRU is prohibitively expensive – “almost always” discards one of the most LRU lines and no guarantee it was the absolutely LEAST recently used is sufficient
2WSA for caches where even PLRU is too slow – address of an item is used to put it in one of two positions, and the LRU of those two is discarded
Direct mapped evicts whatever was in that position before it, regardless of when it was last used

## Slide 13: Cache Write Strategies
Write through: changed cache line immediately goes back to main memory
Write back: cache line is marked when dirty, eviction sends back to main memory
Write combining: grouped writes of cache lines back to main memory
Uncacheable: dynamic values that can change without warning
Notes: Write through caching: slow, but predictable, resulting in lots of FSB traffic
Write back caching: mark flag bit as dirty, when evicted the processor notes and sends cache line back to main memory, instead of just dropping it; have to be careful of false sharing and cache coherency
Write combining caching: used by graphics cards, groups writes to main memory for speed
Uncacheable: dynamic memory values that can change without warning, used for commodity hardware

## Slide 14: Exclusive versus Inclusive
Only relevant below L3
AMD is exclusive
  Progressively more costly due to eviction
  Can hold more data
  Bulldozer uses "write through" from L1d back to L2
Intel is inclusive
  Can be better for inter-processor memory sharing
  More expensive as lines in L1 are also in L2 & L3
  If evicted in a higher level cache, must be evicted below as well
Notes: In an exclusive cache (AMD), when the processor needs data it is loaded by cache line into L1d, which evicts a line to L2, which evicts a line to L3, which evicts a line to main memory; each eviction is progressively more expensive
Exclusive is necessary if the L2 is less than 4-8x the size of L1, otherwise duplication of data affects L2’s local hit rate
In an inclusive cache (Intel), eviction is much faster - if another processor wants to delete data, it only has to check L2 because it knows L1 will have it as well; exclusive will have to check both, which is more expensive; good for snooping

## Slide 15: Inter-Socket Communication
GT/s – gigatransfers per second
Quick Path Interconnect (QPI, Intel) – 8GT/s
HyperTransport (HTX, AMD) – 6.4GT/s (?)
Both transfer 16 bits per transmission in practice, but Sandy Bridge is really 32
Notes: For intra-socket communication, Sandy Bridge has a 4-ring architecture linking cores, LLC and GPU; prior to Sandy Bridge, required direct linkages
GT/s - how many times signals are sent per second
Not a bus, but a point to point interface for connections between sockets in a NUMA platform, or from processors to I/O and peripheral controllers
DDR = double data rate, two data transferred per clock cycle,
Processors "snoop" on each other, and certain actions are announced on external pins to make changes visible to others; the address of the cache line is visible through the address bus
Sandy Bridge can transfer on both the rise & fall of the clock cycle and is full duplex
HTX could theoretically be up to 32 bits per transmission, but hasn't been done yet that I know of

## Slide 16: MESI+F Cache Coherency Protocol
Specific to data cache lines
Request for Ownership (RFO), when a processor tries to write to a cache line
Modified, the local processor has changed the cache line, implies only one who has it
Exclusive, one processor is using the cache line, not modified
Shared, multiple processors are using the cache line, not modified
Invalid, the cache line is invalid, must be re-fetched
Forward, designate to respond to requests for a cache line
All processors MUST acknowledge a message for it to be valid
Notes: Request for Ownership (RFO): a cache line is held exclusively for read by one processor, but another requests for write; cache line is sent, but not marked shared by the original holder - it is marked Invalid and the other cache becomes Exclusive. This marking happens in the memory controller. Performing this operation in the last level cache is expensive, as is the I->M transition. If a Shared cache line is modified, all other views of it must be marked invalid via an announcement RFO message. If Exclusive, no need to announce.
Processors will try to keep cache lines in an exclusive state, as the E to M transition is much faster than S to M. RFOs occur when a thread is migrated to another processor and the cache lines have to be moved once, or when two threads absolutely must share a line; the costs are a bit smaller when shared across two cores on the same processor.
Collisions on the bus can happen, latency can be high with NUMA systems, sheer traffic can slow things down - all reasons to minimize traffic.
Since code almost never changes, instruction caches do not use MESI but rather just a SI protocol. If code does change, a lot of pessimistic assumptions have to be made by the controller.

## Slide 17: Static RAM (SRAM)
Requires 6-8 pieces of circuitry per datum
Cycle rate access, not quite measurable in time
Uses a relatively large amount of power for what it does
Data does not fade or leak, does not need to be refreshed/recharged
Notes: The number of circuits per datum means that SRAM can never be dense.

## Slide 18: Dynamic RAM (DRAM)
Requires 2 pieces of circuitry per datum
“Leaks” charge, but not sooner than 64ms
Reads deplete the charge, requiring subsequent recharge
Takes 240 cycles (~100ns) to access
Intel's Nehalem architecture - each CPU socket controls a portion of RAM, no other socket has direct access to it
Notes: One transistor, one capacitor
Reading contiguous memory is faster than random access due to how you read - you get one write combining buffer at a time from each of the memory banks, 33% slower. 240 cycles to get data from here
E7-8870 (Westmere) can hold 4TB of RAM, E5-2600 Sandy Bridge "only" 1TB
DDR3-SDRAM:
  Double Data Rate, Synchronous Dynamic
  Has a high-bandwidth three-channel interface
  Reduces power consumption 30% over DDR2
  Data is transferred on the rising and falling edges of a 400-1066 MHz I/O clock of the system
  DDR4 and 5 are coming, or are here with GPGPUs. DDR3L is for lower energy usage

## Slide 19
Architectures

## Slide 20: Current Processors
Intel
  Nehalem/Westmere
  Sandy Bridge
  Ivy Bridge
AMD
  Bulldozer
Oracle
  UltraSPARC isn't dead
Notes: Westmere was the 32nm die shrink of Nehalem from 45nm. Ivy Bridge uses 22nm, but the Sandy Bridge architecture
I'm ignoring Oracle SPARC here, but note that Oracle is supposedly building a 16K core UltraSPARC 64
Current Intel top of the line is Xeon E7-8870 (8 cores per socket, 32MB L3, 4TB RAM), but it's a Westmere-based microarchitecture and doesn’t have the Sandy Bridge improvements
The E5-2600 Romley is the top shelf new Sandy Bridge offering - it's specs don't sound as mighty (8 cores per socket, max 30MB L3, 1TB RAM). Don't be fooled, the Direct Data IO makes up for it as disks network cards can do DMA (Direct Memory Access) from L3, not RAM, decreasing latency by ~18%. Also has two memory read ports, whereas previous architectures only had one and were a bottleneck for math-intensive applications
Sandy Bridge is 4-30MB (8MB is currently max for mobile platforms, even with Ivy Bridge), includes the processor graphics

## Slide 22: “Latency Numbers Everyone Should Know”
L1 cache reference ......................... 0.5 ns
Branch mispredict ............................ 5 ns
L2 cache reference ........................... 7 ns
Mutex lock/unlock ........................... 25 ns
Main memory reference ...................... 100 ns
Compress 1K bytes with Zippy ............. 3,000 ns = 3 µs
Send 2K bytes over 1 Gbps network ....... 20,000 ns = 20 µs
SSD random read ........................ 150,000 ns = 150 µs
Read 1 MB sequentially from memory ..... 250,000 ns = 250 µs
Round trip within same datacenter ...... 500,000 ns = 0.5 ms
Read 1 MB sequentially from SSD* ..... 1,000,000 ns = 1 ms
Disk seek ........................... 10,000,000 ns = 10 ms
Read 1 MB sequentially from disk .... 20,000,000 ns = 20 ms
Send packet CA->Netherlands->CA .... 150,000,000 ns = 150 ms
Shamelessly cribbed from this gist: https://gist.github.com/2843375, originally by Peter Norvig and amended by Jeff Dean
Notes: The problem with these numbers is that while they're not far off, the lowest level cache interactions (registers, store buffers, L0, L1) are truly measured in cycles, not time
Clock cycles are also known as Fetch and Execute or Fetch-Decode-Execute Cycle (FDX), retrieve instruction from memory, determine actions required and carry them out; ~1/3 of a nanosecond

## Slide 23: Measured Cache Latencies
Sandy Bridge-E L1d L2 L3 Main
=======================================================================
Sequential Access ..... 3 clk 11 clk 14 clk 6ns
Full Random Access .... 3 clk 11 clk 38 clk 65.8ns
SI Software's benchmarks: http://www.sisoftware.net/?d=qa&f=ben_mem_latency
Notes: Sandy Bridge has 2 load/store operations for each memory channel
Low values are because the pre-fetcher is hiding real latency in these tests when “striding” memory

## Slide 24: Registers
On-core for instructions being executed and their operands
Can be accessed in a single cycle
There are many different types
A 64-bit Intel Nehalem CPU had 128 Integer & 128 floating point registers
Notes: Types of registers include:
  instruction
  data (floating point, integer, chars, small bit arrays, etc)
  address
  conditional
  constant
  etc.

## Slide 25: Store Buffers
Hold data for Out of Order (OoO) execution
Fully associative
Prevent “stalls” in execution on a thread when the cache line is not local to a core on a write
~1 cycle
Notes: Store buffers disambiguate memory access and manage dependencies for instructions occurring out of program order
If CPU 1 needs to write to cache line A but doesn't have the line in its L1, it can drop the write in the store buffer while the memory controller fetches it to avoid a stall; if line is already in L1 it can store directly to it (and bypass store buffer), possibly causing invalidate requests to be sent out

## Slide 26: Level Zero (L0)
New to Sandy Bridge
A cache of the last 1536 uops decoded
Well-suited for hot loops
Not the same as the older "trace" cache
Notes: Macro ops have to be decoded into micro ops to be handled by the CPU
Nehalem used L1i for macro ops decoding and had a copy of every operand required, but Sandy Bridge caches the uops (Micro-operations), boosting performance in tight code (small, highly profiled and optimized, can be secure, testable, easy to migrate)
Not the same as the older "trace" cache, which stored uops in the order in which they were executed, which meant lots of potential duplication; no duplication in the L0, storing only unique decode instructions
Hot loops (where the program spends the majority of its time) should be sized to fit here

## Slide 27: Level One (L1)
Divided into data and instructions
32K data (L1d), 32K instructions (L1i) per core on a Sandy Bridge
Sandy Bridge loads data at 256 bits per cycle, double that of Nehalem
3-4 cycles to access L1d
Notes: Instructions are generated by the compiler, which knows rules for good code generation
Code has predictable patterns and CPUs are good at recognizing them, which helps pre-fetching
Spatial and temporal locality is good
Nehalem could load 128 bits per cycle, but Sandy Bridge can load double that because load and store address units can be interchanged - thus using 2 128-bit units per cycle instead of one

## Slide 28: Level Two (L2)
256K per core on a Sandy Bridge
2MB per “module” on AMD's Bulldozer architecture
~11 cycles to access
Unified data and instruction caches from here up
If the working set size is larger than L2, misses grow
Notes: When the working set size random access is greater than the L2 size, cache misses start to grow
Caches from L2 up are "unified", having both instructions and data (not in terms of shared across cores)

## Slide 29: Level Three (L3)
Was a “unified” cache up until Sandy Bridge, shared between cores
Varies in size with different processors and versions of an architecture
14-38 cycles to access
Notes: Sandy Bridge allows only exclusive access per core
Last Level Cache (LLC)

## Slide 30
Programming Tips

## Slide 31: Striding & Pre-fetching
Predictable memory access is really important
Hardware pre-fetcher on the core looks for patterns of memory access
Can be counter-productive if the access pattern is not predictable
Martin Thompson blog post: “Memory Access Patterns are Important”
Shows the importance of locality and striding
Notes: Doesn't have to be contiguous in an array, you can be jumping in 2K chunks without a performance hit
As long as it's predictable, it will fetch the memory before you need it and have it staged
Pre-fetching happens with L1d, can happen for L2 in systems with long pipelines
Hardware prefetching cannot cross page boundaries, which slows it down as the working set size increases. If it did and the page wasn't there or is invalid, the OS would have to get involved and the program would experience a page fault it didn't initiate itself
Temporally relevant data may be evicted fetching a line that will not be used

## Slide 32: Cache Misses
Cost hundreds of cycles
Keep your code simple
Instruction read misses are most expensive
Data read miss are less so, but still hurt performance
Write misses are okay unless using Write Through
Miss types:
  Compulsory
  Capacity
  Conflict
Notes: The pre-fetcher will bring data into L1d for you. The simpler your code, the better it can do this
If your code is complex, it will do it wrong, costing a cache miss and forcing it to lose the value of pre-fetching and having to go out to an outer layer to get that instruction again
Compulsory/Capacity/Conflict are miss types

## Slide 33: Programming Optimizations
Stack allocated data is cheap
Pointer interaction - you have to retrieve data being pointed to, even in registers
Avoid locking and resultant kernel arbitration
CAS is better and occurs on-thread, but algorithms become more complex
Match workload to the size of the last level cache (LLC, L3)
Notes: Short lived data is not cheap, but variables scoped within a method running on the JVM are stack allocated and very fast
Think about the affect of contending locking. You've got a warmed cache with all of the data you need, and because of contention (arbitrated at the kernel level), the thread will be put to sleep and your cached data is sitting until you can gain the lock from the arbitrator. Due to LRU, it could be evicted. The kernel is general purpose, may decide to do some housekeeping like defragging some memory, futher polluting your cache. When your thread finally does gain the lock, it may end up running on an entirely different core and will have to rewarm its cache. Everything you do will be a cache miss until its warm again. CAS is better, checking the value before you replace it with a new value. If it's different, re-read and try again. Happens in user space, not at the kernel, all on thread
Algos get a lot harder, though - state machines with many more steps and complexity. And there is still a non-negligible cost. Remember the cycle time diffs for different cache sizes; if the workload can be tailored to the size of the last level cache, performance can be dramatically improved
Note that for large data sets, you may have to be oblivious to caching

## Slide 34: What about Functional Programming?
Have to allocate more and more space for your data structures, leads to eviction
When you cycle back around, you get cache misses
Choose immutability by default, profile to find poor performance
Use mutable data in targeted locations
Notes: Eventually, caches have to evict, cache misses cost hundreds of cycles

## Slide 35: Hyperthreading
Great for I/O-bound applications
If you have lots of cache misses
Doesn't do much for CPU-bound applications
You have half of the cache resources per core
Notes: Hyperthreading shares all CPU resources except the register set
Intel CPUs limit to two threads per core, allows one hyper thread to access resources (like the arithmetic logic unit) while another hyper thread is delayed, usually by memory access. Only more efficient if the combined runtime is lower than a single thread, possible by overlapping wait times for different memory access that would ordinarily be sequential. The only variable is the number of cache hits
Note that the effectively shared L1d & L2 reduce the available caches and bandwidth for each thread to 50% when executing two completely different threads of execution (questionable unless the caches are very large), inducing more cache misses, therefore hyper threading is only useful in a limited set of situations. Can be good for debugging with SMT (simultaneous multi-threading)
Contrast this with Bulldozer's "modules" (akin to two cores), which has dedicated schedulers and integer units for each thread in a single processor

## Slide 36: Data Structures
BAD: Linked list structures and tree structures
BAD: Java's HashMap uses chained buckets
BAD: Standard Java collections generate lots of garbage
GOOD: Array-based and contiguous in memory is much faster
GOOD: Write your own that are lock-free and contiguous
GOOD: Fastutil library, but note that it's additive
Notes: If n is not very large, an array will beat it for performance
Linked lists and trees have pointer chasing which are bad for striding across 2K cache pre-fetching
Java's hashmap uses chained buckets, where each hash's bucket is a linked list
Clojure/Scala vectors are good, because they have groupings of contiguous memory in use, but do not require all data to be contiguous like Java's ArrayList
Cliff Click has his lock-free library, Boundary has added with their own implementations
Fastutil is additive, no removal, but that's not necessarily a bad thing with proper tombstoning and data cleanup

## Slide 37: Application Memory Wall & GC
Tremendous amounts of RAM at low cost
GC will kill you with compaction
Use pauseless GC
  IBM's Metronome, very predictable
  Azul's C4, very performant
Notes: We can have as much RAM/heap space as we want now. And requirements for RAM grow at about 100x per decade. But are we now bound by GC? You can get 100GB of heap, but how long do you pause for marking/remarking phases and compaction? Even on a 2-4 GB heap, you're going to get multi-second pauses - when and how often?
IBM Metronome collector is very predictable.
Azul around one millisecond for lots of garbage with C4.

## Slide 38: Using GPUs
Remember, locality matters!
Need to be able to export a task with data that does not need to update
Notes: Graphics card processing (OpenCL) is great for specific kinds of operations, like floating point arithmetic. But they don't perform well for all operations, and you have to get the data to them.

## Slide 39
The Future

## Slide 40: ManyCore
David Ungar says > 24 cores, generally many 10s of cores
Really gets interesting above 1000 cores
Cache coherency won't be possible
Non-deterministic
Notes: Number of cores is large enough that traditional multi-processor techniques are no longer efficient[citation needed] — largely because of issues with congestion in supplying instructions and data to the many processors.
Network-on-chip technology may be advantageous above this threshold

## Slide 41: Memristor
Non-volatile, static RAM, same write endurance as Flash
200-300 MB on chip
Sub-nanosecond writes
Able to perform processing?
Multistate, not binary
Notes: From HP, due to come out this year or next, may change memory fundamentally.
If the data and the function are together, you get the highest throughput and lowest latency possible.
Could replace DRAM and disk entirely.
When current flows in one direction through the device, the electrical resistance increases; and when current flows in the opposite direction, the resistance decreases. When the current is stopped, the component retains the last resistance that it had, and when the flow of charge starts again, the resistance of the circuit will be what it was when it was last active.
Is write endurance good enough for anything but storage?

## Slide 42: Phase Change Memory (PRAM)
Higher performance than today's DRAM
Intel seems more fascinated by this, just released its "neuromorphic" chip design
Not able to perform processing
Write degradation is supposedly much slower
Was considered susceptible to unintentional change, maybe fixed?
Notes: Thermally-driven phase change, not an electronic process.
Faster because it doesn't need to erase a block of cells before writing.
Flash degrades at 5000 writes per sector, where PRAM lasts 100 million writes.
Some argue that PRAM should be considered a memristor as well.

## Slide 43
Thanks!

## Slide 44: Credits!
What Every Programmer Should Know About Memory, Ulrich Drepper of RedHat, 2007
Java Performance, Charlie Hunt
Wikipedia/Wikimedia Commons
AnandTech
The Microarchitecture of AMD, Intel and VIA CPUs
Everything You Need to Know about the Quick Path Interconnect, Gabriel Torres/Hardware Secrets
Inside the Sandy Bridge Architecture, Gabriel Torres/Hardware Secrets
Martin Thompson's Mechanical Sympathy blog and Disruptor presentations
The Application Memory Wall, Gil Tene, CTO of Azul Systems
AMD Bulldozer/Intel Sandy Bridge Comparison, Gionatan Danti
SI Software's Memory Latency Benchmarks
Martin Thompson and Cliff Click provided feedback &additional content